## Slide 1: Introduction to Computer Networks
Lecture 1

## Slide 2: Textbook / References
“Behrouz A Forouzan” - Data Communications and Networking.
“Behrouz A Forouzan” – TCP/IP protocols suite
“D. Comer”- Internetworking with TCP/IP
“Kurose Ross”-Computer Networking A Top-Down Approach

## Slide 4: Networking Devices

## Slide 17: Network topology

## Slide 18: Topology
Topology refers to the layout of connected devices on a network.
Here, some logical layout of topology.
      Mesh
      Star
      Bus
      Ring

## Slide 19: Network Topology

## Slide 20: Mesh Topology
Here every device has a point to point link to every other device.
Node 1 node must be connected with n-1 nodes.
A fully connected mesh can have n(n-1)/2 physical channels to link n devices.
It must have n-1 I/O ports.

## Slide 21: Mesh Topology
Advantages:
They use dedicated links so each link can only carry its own data load. So traffic problem can be avoided.
It is robust. If any one link get damaged it cannot affect others.
It gives privacy and security.(Message travels along a dedicated link)
Fault identification and fault isolation are easy.

## Slide 22: Mesh Topology

## Slide 23: Mesh Topology
Disadvantages:
The amount of cabling and the number of I/O ports required are very large. Since every device is connected to each devices through dedicated links.
The sheer bulk of wiring is larger then the available space.
Hardware required to connected each device is highly expensive.

## Slide 24: Mesh Topology
Applications:
Telephone Regional office.
WAN.(Wide Area Network).

## Slide 25: Star Topology
Here each device has a dedicated point-to-point link to the central controller called “Hub”(Act as a Exchange).
There is no direct traffic between devices.
The transmission are occurred only through the central “hub”.
When device 1 wants to send data to device 2; First sends the data to hub. Which then relays the data to the other connected device.

## Slide 26: Star Topology

## Slide 27: Star Topology
Advantages:
Less expensive then mesh since each device is connected only to the hub.
Installation and configuration are easy.
Less cabling is need then mesh.
Robustness.(if one link fails, only that links is affected. All other links remain active)
Easy to fault identification & to remove parts.
No distruptions to the network then connecting(or) removing devices.

## Slide 28: Star Topology
Disadvantages:
Even it requires less cabling then mesh when compared with other topologies it still large.(Ring or bus).
Dependency(whole n/w dependent on one single point(hub). When it goes down. The whole system is dead.

## Slide 29: Applications
Star topology used in Local Area Networks(LANs).
High speed LAN often used STAR.

## Slide 30: Bus Topology
A bus topology is multipoint.
Here one long cable act as a backbone to link all the devices are connected to the backbone by drop lines and taps.
Drop line- is the connection b/w the devices and the cable.
Tap- is the splitter that cut the main link.
This allows only one device to transmit at a time.

## Slide 31: Bus Topology

## Slide 32: Bus Topology
A device want to communicate with other device on the n/ws sends a broadcast message onto the wire all other devices see.
But only the intended devices accepts and process the message.

## Slide 33: Bus Topology
Advantages:
Ease of installation
Less cabling
Disadvantages:
Difficult reconfiguration and fault isolation.
Difficult to add new devices.
Signal reflection at top can degradation in quality.
If any fault in backbone can stops all transmission.

## Slide 34: Bus Topology
Applications:
Most computer motherboard.

## Slide 35: Ring Topology
Here each device has a dedicated connection with two devices on either side.
The signal is passed in one direction from device to device until it reaches the destination and each device have repeater.
When one device received signals instead of intended another device, its repeater then regenerates the data and passes them along.
To add or delete a device requires changing only two connections.

## Slide 36: Ring Topology

## Slide 37: Ring Topology
Advantages:
Easy to install.
Easy to reconfigure.
Fault identification is easy.
Disadvantages:
Unidirectional traffic.
Break in a single ring can break entire network.

## Slide 38: Ring Topology
Applications:
Ring topologies are found in some office buildings or school campuses.
Today high speed LANs made this topology less popular.

## Slide 39
Data communications are the exchange of data between two devices via some form of transmission medium such as a wire cable. For data communications to occur, the communicating devices must be part of a communication system made up of a com­bination of hardware (physical equipment) and software (programs).
Basic Data Communication

## Slide 40
A data communications system has five components:
1. Message: The message is the information (data) to be communicated. Popular forms of information include text, numbers, pictures, audio, and video.
2. Sender: The sender is the device that sends the data message. It can be a com­puter, workstation, telephone handset, video camera, and so on.
3. Receiver: The receiver is the device that receives the message. It can be a com­puter, workstation, telephone handset, television, and so on.
4. Transmission medium: The transmission medium is the physical path by which a message travels from sender to receiver. Some examples of transmission media include twisted-pair wire, coaxial cable, fiber-optic cable, and radio waves.
5. Protocol: A protocol is a set of rules that govern data communications. It repre­sents an agreement between the communicating devices. Without a protocol, two devices may be connected but not communicating, just as a person speaking French cannot be understood by a person who speaks only Japanese.
Basic Data Communication cont.