## Slide 1: 12
Inventory Management

## Slide 2: Learning Objectives
Define the term inventory and list the major reasons for holding inventories; and list the main requirements for effective inventory management.
Discuss the nature and importance of service inventories
Discuss periodic and perpetual review systems.
Discuss the objectives of inventory management.
Describe the A-B-C approach and explain how it is useful.

## Slide 3: Learning Objectives
Describe the basic EOQ model and its assumptions and solve typical problems.
Describe the economic production quantity model and solve typical problems.
Describe the quantity discount model and solve typical problems.
Describe reorder point models and solve typical problems.
Describe situations in which the single-period model would be appropriate, and solve typical problems.

## Slide 4: Inventory
Independent Demand
A
B(4)
C(2)
D(2)
E(1)
D(3)
F(2)
Dependent Demand
Independent demand is uncertain. Dependent demand is certain.
Inventory: a stock or store of goods

## Slide 5: Inventory Models
Independent demand – finished goods, items that are ready to be sold
  E.g. a computer
Dependent demand – components of finished products
  E.g. parts that make up the computer

## Slide 6: Types of Inventories
Raw materials & purchased parts
Partially completed goods called work in progress
Finished-goods inventories
  (manufacturing firms) or merchandise (retail stores)

## Slide 7: Types of Inventories (Cont’d)
Replacement parts, tools, & supplies
Goods-in-transit to warehouses or customers

## Slide 8: Functions of Inventory
To meet anticipated demand
To smooth production requirements
To decouple operations
To protect against stock-outs

## Slide 9: Functions of Inventory (Cont’d)
To take advantage of order cycles
To help hedge against price increases
To permit operations
To take advantage of quantity discounts

## Slide 10: Objective of Inventory Control
To achieve satisfactory levels of customer service while keeping inventory costs within reasonable bounds
  Level of customer service
  Costs of ordering and carrying inventory
Inventory turnover is the ratio of average cost of goods sold to average inventory investment.

## Slide 11: Effective Inventory Management
A system to keep track of inventory
A reliable forecast of demand
Knowledge of lead times
Reasonable estimates of
  Holding costs
  Ordering costs
  Shortage costs
A classification system

## Slide 12: Inventory Counting Systems
Periodic System
  Physical count of items made at periodic intervals
Perpetual Inventory System System that keeps track of removals from inventory continuously, thus monitoring current levels of each item

## Slide 13: Inventory Counting Systems (Cont’d)
Two-Bin System - Two containers of inventory; reorder when the first is empty
Universal Bar Code - Bar code printed on a label that has information about the item to which it is attached
0
214800 232087768

## Slide 14: Key Inventory Terms
Lead time: time interval between ordering and receiving the order
Holding (carrying) costs: cost to carry an item in inventory for a length of time, usually a year
Ordering costs: costs of ordering and receiving inventory
Shortage costs: costs when demand exceeds supply

## Slide 15: ABC Classification System
Classifying inventory according to some measure of importance and allocating control efforts accordingly.
  A - very important
  B - mod. important
  C - least important
Figure 12.1
Annual
$ value
of items
A
B
C
High
Low
Low
High
Percentage of Items

## Slide 16: Cycle Counting
A physical count of items in inventory
Cycle counting management
  How much accuracy is needed?
  When should cycle counting be performed?
  Who should do it?

## Slide 17: Economic Order Quantity Models
Economic order quantity (EOQ) model
  The order size that minimizes total annual cost
Economic production model
Quantity discount model

## Slide 18: Assumptions of EOQ Model
Only one product is involved
Annual demand requirements known
Demand is even throughout the year
Lead time does not vary
Each order is received in a single delivery
There are no quantity discounts

## Slide 19: The Inventory Cycle
Figure 12.2
Profile of Inventory Level Over Time
Quantity
on hand
Q
Receive
order
Place
order
Receive
order
Place
order
Receive
order
Lead time
Reorder
point
Usage
rate
Time

## Slide 20: Total Cost
Annual
carrying
cost
Annual
ordering
cost
Total cost =
+
TC =
Q
2
H
D
Q
S
+

## Slide 21: Cost Minimization Goal
Order Quantity (Q)
The Total-Cost Curve is U-Shaped
Ordering Costs
QO
Annual Cost
(optimal order quantity)
Figure 12.4C

## Slide 22: Deriving the EOQ
Using calculus, we take the derivative of the total cost function and set the derivative (slope) equal to zero and solve for Q.